## Slide 1: Classification of Motor Imagery EEG Data on the stm32 mcu and the gapuino board
Machine Learning on Microcontrollers Final Project
Alkinoos Sarioglou
20-947-743

## Slide 2: Overview
Dataset: EEG Motor Movement/Imagery Dataset
Goal of the project: Classify the brain signals into 5 classes
  Rest
  Open Right Hand
  Open Left Hand
  Open Both Hands
  Open Both Feet
Classification using Deep Convolutional Neural Network on the STM32 MCU and the GAPUINO board
Potential applications: Prosthetics/Artificial Limbs controlled by thought, Gaming, AR/VR

## Slide 3: Dataset
EEG recordings taken from 109 subjects
Measurements taken using the BCI2000 system (64 electrodes)
For each subject 6 experimental rounds were examined:
  3 times of 2 rounds:
    1 round of imagining opening and closing the left or right hand
    1 round of imagining opening and closing both hands or both feet
Classification Classes:
  Rest {0}
  Left Hand {1}
  Right Hand {2}
  Both Hands {3}
  Both Feet {4}

## Slide 4: Approach for Training, Validation and Testing Datasets
Steps:
  For each task (e.g. Rest) take the Short-Time Fourier Transform (STFT) – 10 windows over 4 seconds
  Extract the Fourier Coefficients of the Delta, Mu and Beta frequency bands for each electrode:
    Delta band = 0.5 – 4 Hz
    Mu band = 8 – 13 Hz
    Beta band = 13 – 30 Hz
  For each band of each electrode the sum of the squared absolute values is calculated
  The result of each band is assigned to the R,G,B channels of a pixel, where each pixel represents a single electrode:
    R = Delta Band
    G = Mu Band
    B = Beta Band
  Output of 64 (R,G,B) pixels - each pixel represents an electrode
  1 image per window – 10 images per task
  300 images per round (30 tasks)
  185400 images in total (300 images x 6 rounds x 109 subjects)

## Slide 5: Preprocessing Steps
#1: Extract electrode coordinates in mm and convert them to pixel positions in a 32x32 image
Notes: Activation regions become visible

## Slide 6: Preprocessing Steps
#2: Separate subjects depending on the task duration in their measurements - 4 groups of subjects
Group A
Group B
Group C
Group D

## Slide 7: Preprocessing Steps
#3: Define appropriate windows to examine with the STFT depending on the subject group

## Slide 8: Preprocessing Steps
#4: Read every file and perform STFT for all the windows
  Extract Delta, Mu and Beta bands for each window
  Perform sum of squares of the coefficients
  Assign these values to the R, G, B channels of a pixel
  Repeat for every electrode to get 64 pixels

## Slide 9: Preprocessing Steps
#5: Assign pixel values to coordinates of the corresponding electrodes
Interpolate between the electrodes (Cubic) to get the full image

## Slide 10: Training, Validation, Testing Datasets
Training Dataset: 185400 32x32 RGB images
Validation Dataset: 1800 32x32 RGB images
Testing Dataset: 1800 32x32 RGB images

## Slide 11: Implementation problems
Problem #1: Unbalanced Dataset – Class 0 dominates the dataset
The distribution of samples:
Class 0
Class 1
Class 2
Class 3
Class 4
Problem #2: CNN with LSTM model proposed by the research paper OVERFITS – Test Accuracy: 50% but NOT USEFUL, just predictions of Class 0
Problem #3: Also consumes a lot of memory!
  STM32 – TFLite micro
Proposed Model by Research Paper
Conv2D(64)
Conv2D(64)
Conv2D(64)
MaxPooling2D
Conv2D(128)
Conv2D(128)
MaxPooling2D
Conv2D(256)
Conv2D(256)
ReLU
MaxPooling2D
LSTM(256)
Dense(5)

## Slide 12: Implementation and Optimization
Solution #2: Remove complexity to fit the memory requirements of the STM32 MCU (STM32 Flash: 1024 KiB, STM32 RAM: 96 KiB) and the GAPUINO board (GAPUINO L1: 48 kB, L2: 307.2 kB, L3: 8.3 MB)
Steps taken:
  Less layers
  Less filters applied per Convolutional 2D layer
  Less LSTM cells
Solution #1: Undersampling all classes apart from minority Class 2 - Create a balanced dataset
New organisation of samples: 10 Class 0, 10 Class 1, 10 Class 2, 10 Class 3, 10 Class 4, …
New distribution of samples:
Class 0
Class 1
Class 2
Class 3
Class 4

## Slide 13: Architecture - 1
Conv2D(32)
BatchNormalization()
SpatialDropout2D(0.5)
ReLU()
MaxPooling2D(2,2)
Conv2D(64)
BatchNormalization()
SpatialDropout2D(0.5)
ReLU()
MaxPooling2D(2,2)
Conv2D(64)
BatchNormalization()
SpatialDropout2D(0.5)
ReLU()
MaxPooling2D(2,2)
Flatten
Dense(5)
LR = 0.01
Batch size = 8
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 40.22%
Final Loss = 1.5317
Quantized Model - Memory STM32 (Flash) = 57.05 KiB (5.57%)
Quantized Model - Memory STM32 (RAM) = 33.36 KiB (34.75%)
TFLite micro TensorArena size = 66336 bytes
STM32CubeAI speed =
  164.875 ms (average duration)
  13189977 (average CPU cycles)
  2.86 cycles/MACC
TFLite micro speed = 33872661 CPU cycles
Notes: TFLite micro more cycles because of Spatial Dropout 2D
Added Dropout to avoid overfitting
SpatialDropout2D drops entire 2D feature maps instead of individual elements

## Slide 14: Architecture - 2
Conv2D(32, kernel size = (2,2), stride= (2,2))
Conv2D(64, kernel size = (2,2), stride = (2,2))
Conv2D(64, kernel size = (2,2), stride = (2,2))
Flatten
Dense(5)
LR = 0.01
Batch size = 8
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 33.28%
Final Loss = 1.5864
Quantized Model - Memory STM32 (Flash) = 30.02 KiB (2.93%)
Quantized Model - Memory STM32 (RAM) = 17.94 KiB (18.69%)
TFLite micro TensorArena size = 18000 bytes
Memory GAPUINO = 44620 (Bytes in L1), 43421 (Bytes in L2), 0 (Bytes in L3)
STM32CubeAI speed =
  124.58 ms (average duration)
  9966411 (average CPU cycles)
  11.03 cycles/MACC
TFLite micro speed = 3971615 CPU cycles
GAPUINO speed =
  1348719 (Cycles)
  904197 (Operations)
  0.6704 (Operations/Cycle)
Notes: This can be run both on STM32 and Gapuino

## Slide 15: Architecture - 3
Conv2D(32)
MaxPooling2D (2,2)
Conv2D(64)
MaxPooling2D (2,2)
Conv2D(128)
Flatten
Dense(5)
LR = 0.01
Batch size = 1
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 25.5%
Final Loss = 1.7893
Quantized Model - Memory STM32 (Flash) = 94.24 KiB (9.2%)
Quantized Model - Memory STM32 (RAM) = 19.10 KiB (19.9%)
TFLite micro TensorArena size = 43536 bytes
Memory GAPUINO = 47532 (Bytes in L1), 106525 (Bytes in L2), 0 (Bytes in L3)
STM32CubeAI speed =
  642 ms (average duration)
  51375400 (average CPU cycles)
  9.96 cycles/MACC
TFLite micro speed = 20976017 CPU cycles
GAPUINO speed =
  934891 (Cycles)
  4664613 (Operations)
  4.99 (Operations/Cycle)

## Slide 16: Architecture - 4
Conv2D(32)
BatchNormalization()
ReLU()
MaxPooling2D(2,2)
Conv2D(64)
BatchNormalization()
ReLU()
MaxPooling2D(2,2)
Conv2D(64)
BatchNormalization()
ReLU()
MaxPooling2D(2,2)
Flatten
Dense(5)
LR = 0.01
Batch size = 8
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 28.67%
Final Loss = 1.7149
Quantized Model - Memory STM32 (Flash) = 57.05 KiB (5.57%)
Quantized Model - Memory STM32 (RAM) = 33.36 KiB (34.75%)
TFLite micro TensorArena size = 66336 bytes
STM32CubeAI speed =
  164.875 ms (average duration)
  13189977 (average CPU cycles)
  2.86 cycles/MACC
TFLite micro speed = 33954102 CPU cycles

## Slide 17: Architecture - 5
TimeDistributed(Conv2D(64))
TimeDistributed(BatchNormalization)
TimeDistributed(ReLU)
TimeDistributed(MaxPooling2D(2,2))
TimeDistributed(Conv2D(128))
TimeDistributed(BatchNormalization)
TimeDistributed(ReLU)
TimeDistributed(MaxPooling2D(2,2))
TimeDistributed(Conv2D(128))
TimeDistributed(BatchNormalization)
TimeDistributed(ReLU)
TimeDistributed(MaxPooling2D(2,2))
TimeDistributed(Flatten)
LSTM(8)
Dense(5)
LR = 0.01
Batch size = 10
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 39.28%
Final Loss = 1.9709

## Slide 18: Comparison Plots – Accuracy / loss
Chart: Accuracy Comparison
| 1 | 2 | 3 | 4 | 5
Accuracy | 40.22 | 33.28 | 25.5 | 28.67 | 39.28
Chart: Loss Comparison
| 1 | 2 | 3 | 4 | 5
Loss | 1.5317 | 1.5864 | 1.7893 | 1.7149 | 1.9709

## Slide 19: Comparison Plots – STM32
Chart: STM32Cube average CPU cycles - Comparison
STM32Cube average CPU cycles | 13189977 | 9966411 | 51375400 | 13189977
Chart: TFLite micro CPU cycles - Comparison
TFLite micro CPU cycles | 33872661 | 3971615 | 20976017 | 33954102
Chart: STM32 Memory Flash - Comparison
STM32 Memory Flash | 57.05 | 30.02 | 94.24 | 57.05
Chart: STM32 Memory RAM - Comparison
STM32 Memory RAM | 33.36 | 17.94 | 19.1 | 33.36

## Slide 20: selected model – stm32
Architecture 1
Conv2D(32)
BatchNormalization()
SpatialDropout2D(0.5)
ReLU()
MaxPooling2D(2,2)
Conv2D(64)
BatchNormalization()
SpatialDropout2D(0.5)
ReLU()
MaxPooling2D(2,2)
Conv2D(64)
BatchNormalization()
SpatialDropout2D(0.5)
ReLU()
MaxPooling2D(2,2)
Flatten
Dense(5)
LR = 0.01
Batch size = 8
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 40.22%
Final Loss = 1.5317
Quantized Model - Memory STM32 (Flash) = 57.05 KiB (5.57%)
Quantized Model - Memory STM32 (RAM) = 33.36 KiB (34.75%)
TFLite micro TensorArena size = 66336 bytes
STM32CubeAI speed =
  164.875 ms (average duration)
  13189977 (average CPU cycles)
  2.86 cycles/MACC
TFLite micro speed = 33872661 CPU cycles

## Slide 21: Comparison Plots – gapuino
Chart: GAPUINO Cycles - Comparison
| 2 | 3
GAPUINO Cycles | 1348719 | 934891
Chart: GAPUINO Operations - Comparison
| 2 | 3
GAPUINO Operations | 904197 | 4664613
Chart: GAPUINO Memory - Comparison
| 2 | 3
GAPUINO Memory | 88041 | 154057
Chart: GAPUINO Operations/Cycle - Comparison
| 2 | 3
GAPUINO Operations/Cycle | 0.6704 | 4.99

## Slide 22: selected model – gapuino
Architecture 2
Conv2D(32, kernel size = (2,2), stride= (2,2))
Conv2D(64, kernel size = (2,2), stride = (2,2))
Conv2D(64, kernel size = (2,2), stride = (2,2))
Flatten
Dense(5)
LR = 0.01
Batch size = 8
Epochs = 20
Optimizer = SGD
Loss function = Sparse Categorical Crossentropy
Final Accuracy = 33.28%
Final Loss = 1.5864
Quantized Model - Memory STM32 (Flash) = 30.02 KiB (2.93%)
Quantized Model - Memory STM32 (RAM) = 17.94 KiB (18.69%)
TFLite micro TensorArena size = 18000 bytes
Memory GAPUINO = 44620 (Bytes in L1), 43421 (Bytes in L2), 0 (Bytes in L3)
STM32CubeAI speed =
  124.58 ms (average duration)
  9966411 (average CPU cycles)
  11.03 cycles/MACC
TFLite micro speed = 3971615 CPU cycles
GAPUINO speed =
  1348719 (Cycles)
  904197 (Operations)
  0.6704 (Operations/Cycle)

## Slide 23: Thank you for your time and attention!